Adjusting entrance door

The two striker bolts which protrude from the door frame should be tight.  Once they are tight you should be able to grab either striker bolt and with a some effort, the bolts, along with the back plate, should move up and down.  If the bolts are to tight they will not 'float' and won't properly adjust and align with the door when closed.

Whenever my door doesn't close properly one or both of the bolts came loose.  I tighten them down, back off a quarter turn then make sure they move up and down.
This has always worked for me.

It's also possible your handle and lock needs adjusting.

See PDF on handle adjustment

Adjustments are performed by a nut on the rods that is turned to either lengthen or shorten the rod depending on the need.  It could also be the latch mechanism itself; you might try lubricating this with white lithium grease.

Latch Adjustments

Adjusting the Entry Door Latch:

Determine which bolt needs adjustment.

Slowly close the entry door, observing the latch and strike bolt alignment.  DO NOT attempt to latch if the alignment is off.  If the alignment is correct, allow the latch to catch in the first (primary) position only.

The latch should move to the second position with only slight pressure applied to the entry door.  Upper and lower latches should be evenly timed. Press on the entry door to check for further movement.

The entry handle should operate with little effort to open the entry door.  Excess pressure indicates the bolts are set too far back.

With a box wrench or socket, loosen the movable strike bolt.  Make all adjustments in small increments. Tighten the bolt firmly after making adjustments.  The bolts should have slight up and down movement for vibration control in travel.

Test the operation of the dead bolt lock to ensure proper functions.

Apply silicone weekly to the entry door rubber gaskets to prevent squeaking while the motorhome is in use.  Use a 1" sponge paint brush, sprayed with silicone for easy application.

CAUTION:

When operating the entry door, ensure the dead bolt latch is fully unlocked prior to closing. Failure to do so can result in damage to the dead bolt and/or entry door.

Latch Adjustments - Adjusting the Entry Door Latch:
Determine which bolt needs adjustment.
Slowly close the entry door, observing the latch and strike bolt alignment.
DO NOT attempt to latch if the alignment is off.
If the alignment is correct, allow the latch to catch in the first
(primary)position only.

The latch should move to the second position with only slight pressure applied
to the entry door.
Upper and lower latches should be evenly timed.
Press on the entry door to check for further movement.

The entry handle should operate with little effort to open the entry door.
Excess pressure indicates the bolts are set too far back.

With a box wrench or socket, loosen the movable strike bolt.
Make all adjustments in small increments.
Tighten the bolt firmly after making adjustments.
The bolts should have slight up and down movement for vibration control in
travel.

Test the operation of the dead bolt lock to ensure proper functions.

Apply silicone weekly to the entry door rubber gaskets to prevent squeaking
while the motorhome is in use.
Use a 1" sponge paint brush, sprayed with silicone for easy application.

CAUTION
When operating the entry door, ensure the dead bolt latch is fully unlocked
prior to closing.
Failure to do so can result in damage to the dead bolt and/or entry door.