Speed calibration for my speedometer.

My Rear Axle Ratio is  4.30:1

My tire size revs per mile is 548.

Engine RPM x 60 ÷ Wheel revs per
mile ÷ rear axle ratio ÷ final drive gear of transmission = Speed in mph

1450*60/548/.43/6 = 61.53454 for my coach

1410RPM at 60MPH according to Silverleaf.  The 1410 varied while
looking at it about +/- 3RPM.